## Slide 1
Robert Delinom
Urbanization and Proposed Adaptive Development Strategies in Megacities : The Greater Jakarta
Robert Delinom
ICIAR – LIPI

## Slide 2
Regionally, Jakarta area is occupied by lowland area that has five main landforms (Rimbaman and Suparan, 1999) that consists of:
Volcanic and alluvial landforms, that are found in southern part of the basin,
Marine origin landforms, which are occupied the northern area adjacent to the coastline,
Beach ridge landforms, which are discovered along the coast with east-west direction,
Swamp and mangrove area landforms, which are encountered in the coastal fringe,
Paleo-channels, which run perpendicular to the coastline.

## Slide 3: JAKARTA GEOLOGICAL CHARACTERISTIC
Genetically, formed in fluviatile, fluvio-marine, fluvio-volcanic or shallow marine environment
As an area with volcanic chain in the hinterland area, it is mostly formed by fluviatile and fluvio-volcanic sediment
Some aquifers found as a lens in beach ridge
Tertiary Formation act as the Basin Basement

## Slide 4
Geological Setting
Simplified Model
(Modified from Iwaco & Ministry Of Public Work, Indonesia ; 1994)
S
N
(Not to scale)

## Slide 5: Greater Jakarta Present Condition
Around 10 millions inhabitant live in Jakarta Area. (During office hours around 12 millions)‏
Urbanization to this city unstoppable
Land Caring Capacity Decreasing
Subsidence occurred
Water resources use is increasing year by year.

## Slide 6
Year | Population ('000) | Year | Population ('000)
1948 | ≈ 2,000 | 2002 | 8,379
1961 | 2,973 | 2003 | 8,603
1971 | 4,579 | 2004 | 8,725
1980 | 6,503 | 2005 | 8,864
1990 | 8,259 | 2006 | 8,961
Population Growth of DKI Jakarta
[Lo and Yeung, 1995; BPS Jakarta, 2007]

## Slide 7
Population
Land use
Jakarta
urbanization

## Slide 8: Greater Jakarta Population Density (people/km2)‏
South Jakarta : 11.676
East Jakarta : 11.157
Central Jakarta : 18.746
West Jakarta : 12.426
North Jakarta : 8.267
Seribu Islands : 1.616
Total Population : 7.456.931 people
Average Density : 11.272 people/km2.
(Sources: BPS Prop. DKI Jakarta, 2003).

## Slide 9
subsidence due to groundwater extraction (including de-watering)
subsidence induced by the load of constructions (i.e. settlement of high compressibility soil),
subsidence caused by natural consolidation of alluvium soil, and
tectonic subsidence.
Land Subsidence in Jakarta

## Slide 11
Step1
Step2
Step3
Step4
Step5
Tokyo
Osaka
Taipei
Bangkok
Jakarta
Step1
Step2
Step3
Step4
Step5
Groundwater demand for the city water (cheep, easy access, stable, clean)
GW disaster followed by urban expansion
(land subsidance, salinization, oxygen deficit air accident, etc）
Enforcement of GW regulation
（groundwater disaster→regulation）
Recovery of regulated area⇔
Maximun potential recharge⇔Hydro-meteorological setting of the city
New GW disaster caused by abrupt recovery
（Floating problem of subsurface station）
Infrastructure of surface water supply
and National groundwater act
（public water of private property ?）
Induced recharge
（shallow aquifer, river & sea water）
Sustainable GW management
considering potential recharge rate

## Slide 12
The decision maker paradigm :
“Out of sight out of mind”
There is always no consideration to groundwater

## Slide 13
LAND SUBSIDENCE ZONATION IN JAKARTA (2002 – 2010)
Land Subsidence Locations in Jakarta :
North Jakarta : Muara Baru, Pantai Mutiara, Pantai Indah Kapuk, dan Ancol ; West Jakarta Barat : Cengkareng Barat ; East Jakarta : Kelapa Gading
116 cm
65 cm
47 cm
11 cm
15 cm
Hasanuddin Z. Abidin, 2010

## Slide 14
0 30km
Land
Subsidence
from InSAR
June 2006
to February 2007
(8 months)
Cooperation with
ERSDAC Japan
Deguchi, 2007
CONES OF SUBSIDENCE
Pantai Mutiara Estate
(Reclamation land)

## Slide 15: IMPACTS OF LAND SUBSIDENCE
The wider expansion of (coastal) flooding areas.
Cracking of buildings and infrastructure.
Lowering the quality of living environment and life (e.g. health and sanitation condition) in the affected areas.
Increasing the maintenance costs for the affected buildings and infrastructure.

## Slide 16
Genangan Rob (Gunung sahari)
Genangan Rob (Tongkol)
Struktur jembatan turun (mutiara)
Bangunan miring (Tongkol)
Genangan Rob (Gunung sahari)
Impacts of Subsidence in Jakarta
Hasanuddin Z. Abidin
KK Geodesi ITB 2010

## Slide 17
Impacts of Coastal Subsidence in Jakarta

## Slide 18
Sea Level Rise in Coastal Areas of Jakarta
Hasanuddin Z. Abidin, 2009
Tide
Gauge
Satellite
Altimetry

## Slide 20
 | CONSERVATIVE SCENARIO | PESIMISTIC SCENARIO
Land subsidence rate | 2.5 cm/year | 10 cm/year
Sea level rise rate | 0.2 cm/year | 1 cm/year
Possible Inundation Areas
in Coastal Areas of Jakarta
Hasanuddin Z. Abidin, 2009

## Slide 21: AIR TEMPERATURE AT JAKARTA
Indonesia Ministry of Environment & NOAA, BMG, 2007
Annual gradient
Hansen and Lebendeff, 1987 ; Huang et.all, 2000 :
1.36 0 C
Global warming : 0.5 – 0.7 0C/100 year
2005

## Slide 22: Distribution Surface Temperature Warming in Jakarta Groundwater Basin
MAXIMUM HIGH DENSITY EFFECT OF HEAT ISLAND /URBANIZATION EFFECT

## Slide 23: Some parameters should be concern :
Jakarta needs more space for living area
Retention Dam
Good, wide, and deep water way
Decrease the air pollution and green environment
An Adaptive Urban Oasis should be created

## Slide 29
Thank you